## Slide 1
Problem and Motivation
Large amounts of data from different sensor types
are needed to obtain a realistic 3-D model of a
large environment.
The manner these sensor data are acquired is usually
constrained (e.g. assume registered data).
How to interpret, combine and integrate the sensory
data when data acquisiton is flexible.
We fuse range and intensity data to obtain geometric
and photometric detail, respectively.
Sensor Fusion for 3­D Modeling of Indoor Environments
L.A. Torres-Méndez and G. Dudek, Centre for Intelligent Machines
http://www.cim.mcgill.ca/~mrl
Conclusions
Our approach is able to fuse two type of sensor data
with a small amount of information.
Using PCA for detecting vertical lines, even
when these lines are noisy, improves the
matching for the registration.
Relationships between range and intensity are
extracted from the inherent characteristics in
indoor environments.
References
[1] A. Fitzgibbon and A. Zisserman. "Automatic 3D model acquisition and generation of new images from video sequences". Proceedings of European Signal Processing Conference, pp. 1261-1269, 1998.
[2] K.N. Kutulakos and S.M. Seitz. "A Theory of Space Carving". University of
Rochester CS Technical Report 692, May 1998.
[3] I. Stamos and P. Allen. "3D Model Construction using range and image data".
Computer Vision and Pattern Recognition Conference, 2000.
Sensor fusion involves registration and
integration of data, and must consider:
Sparse and non-uniform data from sensors
Different resolutions in the unregistered data
Registration
(alignment of the data)
Integration
(one 3-D model )
1. The Method
The mobile robot gathers range and intensity data from different locations and vantage points
Intensity data partly
overlaps with range data
3. Integration
(Ongoing work)
Estimation of range and/or intensity
The algorithm starts by growing the overlapping regions
using information from neighbouring images.
New range and/or intensity values are generated pixel
by pixel , local similarity is preserved .
The Occupancy Grid Model
It fuses intensity and range data
into a common coordinate frame.
Sensor data are projected to
corresponding grid locations.
Ocupancy probabilities and
surface properties are assigned.
Carving away inconsistent voxels
Each voxel is checked for
consistency:
When vision rays and range
rays intersect, their likelihoods
influence one another.
2. Registration
The positions and viewpoints where the intensity and range images are acquired:
Range view
Intensity views
2-D Edge detection
Range view synthesis
based on the intensity viewpositions
Observations:
How much overlapping should exist between range and intensity views?
How many matchings of distances are enough for the registration?
Difficult when few 3-D vertical edges are found in the range views
Uncertainty in the robot pose must be considered due to odometry errors
Matching of distances from both intensity and range views
Vertical lines extracted using PCA
Planar segmentation to extract 3-D Edges
( region growing and surface normal analysis)
Vertical lines extracted using PCA and distances between lines.